## Slide 1
NYC Reservoir Optimization — Objective Definitions
• Many-objective optimization (MM Borg MOEA) of New York City reservoir release and diversion policy in the Delaware River Basin, evaluated with the Pywr-DRB simulation model.
• Each candidate policy (FFMP rule parameters, 24 decision variables) is simulated; objectives are computed from the resulting daily timeseries after dropping the first 365 days (model warm-up).
• Seven active objectives span every DRB stakeholder axis: NYC water supply (2), Montague flow Decree (2), Trenton flow Decree (1), downstream flood exposure (1), and NYC storage resilience (1).
• Two evaluation modes: (a) a single historic streamflow trace (manuscript baseline), and (b) a stochastic ensemble of N short synthetic scenarios scored by satisficing across realizations.
• Goalposts are the static 1954 U.S. Supreme Court Decree quantities, never the time-varying FFMP drought step-down targets — scoring against a live target would reward a policy for lowering its own goalpost.
• Conventions: reliabilities are fractions from 0 to 1; deficits and storage are percentages from 0 to 100; “higher is better” for maximize objectives, “lower is better” for minimize objectives.

## Slide 2
Notation — Plain-Language Building Blocks
shortfall: (gap)₊ = max(gap, 0) — the part of a miss below the goal; never negative
weekly value = the average of that week’s daily values
reliability = (weeks that meet the goal) ÷ (total weeks)
CVaR₉₀(series) = the average of the worst 10% of the weekly values
P₅(series) = the 5th-percentile value (only 5% of days fall below it)
• Flows and demands are in MGD (million gallons per day); storage in MG; percentages are 0–100.
• Decree goalposts (fixed): NYC diversion cap 800 MGD; Montague 1131.05 MGD (= 1750 cfs); Trenton 1938.95 MGD. NYC system capacity = 270,837 MG (Cannonsville + Pepacton + Neversink).
• Ensemble terms: a scenario is one synthetic streamflow realization; N is the number of scenarios; the threshold is the analyst-chosen “acceptable” level for each objective.

## Slide 3
Ensemble Evaluation — Satisficing Across Scenarios
score = (scenarios that pass) ÷ (total scenarios N)
pass = metric ≥ threshold for reliability and storage (higher is better)
pass = metric ≤ threshold for deficits and flood days (lower is better)
• Each single-trace metric is computed on every scenario, then collapsed to the fraction of scenarios that clear that objective’s acceptable threshold.
• All ensemble scores are framed as “higher is better” (a fraction from 0 to 1), whether the underlying metric is a reliability or a deficit / flood count.
• A scenario that produces an invalid (non-finite) value counts as a failure, so a broken run cannot masquerade as acceptable.
• Thresholds are acceptability levels chosen by the analyst, separate from the Decree goalposts inside each metric. Current values are placeholders pending the sensitivity experiment (override via NYCOPT_SAT_THRESHOLDS).
• Satisficing is a stable, fast-converging robustness form for many-objective search under deep uncertainty.
Kasprzyk et al. 2013; Herman et al. 2015; McPhail et al. 2018.

## Slide 4
Objective 1 — NYC Delivery Reliability (higher is better)
demand = min(NYC demand, 800 MGD) [capped at the Decree right]
f₁ = (weeks with delivery ≥ 99% of demand) ÷ (total weeks)
• How often NYC actually receives essentially all of the water it is entitled to draw — a simple success rate over weeks. Compares weekly totals of delivery and demand.
• Demand is capped at the 800 MGD Decree right so voluntary winter low-takes are not counted as shortfalls; only forced failures to meet the right count against the policy.
• Why this form: a success rate is a stable, fast-converging signal for the optimizer, unlike noisier magnitude statistics.
• Ensemble (threshold 0.95): fraction of scenarios whose weekly reliability is at least 0.95.
Hashimoto et al. 1982; Herman et al. 2015; Bonham et al. 2024.

## Slide 5
Objective 2 — NYC Delivery Deficit (lower is better)
weekly deficit = max(demand − delivery, 0) ÷ 800 MGD × 100%
f₂ = average of the worst 10% of weekly deficits (CVaR₉₀)
• How bad the shortfalls get, not just how often they happen: the average size of the worst 10% of weekly supply gaps, as a percent of the 800 MGD cap. Uses weekly averages.
• Each weekly deficit is the amount delivery falls short of capped demand, scaled to the fixed cap so a 50 MGD shortfall reads the same in any season.
• Why the worst-10% average instead of the single worst week: one extreme week is noisy and hard to reproduce; averaging the tail keeps the focus on bad outcomes but is far more stable.
• Ensemble (threshold 10%): fraction of scenarios whose worst-10% deficit is 10% or less.
Rockafellar & Uryasev 2000; Quinn et al. 2017; Fairbrother et al. 2022.

## Slide 6
Objective 3 — Montague Flow Reliability (higher is better)
f₃ = (weeks with Montague flow ≥ 1131.05 MGD) ÷ (total weeks)
1131.05 MGD = 1750 cfs (1954 Decree target)
• How often the river flow at Montague meets NYC’s downstream obligation — again a weekly success rate (using weekly-average flow).
• This will not reach 100%: FFMP drought rules deliberately cut releases below target during droughts, so the achievable ceiling depends on the policy.
• Scored against the fixed Decree target, never the live FFMP target, to avoid rewarding self-lowering drought step-downs.
• Ensemble (threshold 0.85): fraction of scenarios whose weekly reliability is at least 0.85.
Hashimoto et al. 1982; Herman et al. 2015.

## Slide 7
Objective 4 — Montague Flow Deficit (lower is better)
weekly deficit = max(1131.05 − flow, 0) ÷ 1131.05 × 100%
f₄ = average of the worst 10% of weekly deficits (CVaR₉₀)
• How far Montague flow falls below its target in the bad weeks: the average size of the worst 10% of weekly flow gaps, as a percent of the target.
• Montague flow is driven largely by storms, so its single worst week is mostly exogenous noise — the worst-10% average is especially preferable to the single maximum here.
• Each weekly deficit is the shortfall of weekly-average flow below the fixed target, scaled to that target.
• Ensemble (threshold 25%): fraction of scenarios whose worst-10% deficit is 25% or less.
Rockafellar & Uryasev 2000; Quinn et al. 2017.

## Slide 8
Objective 5 — Trenton Flow Reliability (higher is better)
f₅ = (weeks with Trenton flow ≥ 1938.95 MGD) ÷ (total weeks)
• How often flow at Trenton meets the lower-basin / New Jersey obligation — a weekly success rate against the fixed target.
• Replaces an explicit salt-front objective: the Trenton target exists largely to push back salt intrusion (so the two are physically redundant), and Trenton flow is a clean signal whereas the salt-front model is unreliable in extreme drought.
• Ensemble (threshold 0.85): fraction of scenarios whose weekly reliability is at least 0.85.
Hashimoto et al. 1982; Herman et al. 2015.

## Slide 9
Objective 6 — Downstream Flood Days (lower is better)
f₆ = number of days that any tail gauge reaches its NWS minor flood stage
tail gauges: Hale Eddy, Fishs Eddy, Bridgeville
• A simple count of flood-onset days just below the reservoirs: a day counts if any of the three tail gauges hits its minor (flood-onset) stage.
• These gauges respond to NYC’s release decisions — unlike storm-dominated mainstem flow — so flooding here can be attributed to operations.
• Why a day-count: counting threshold exceedances avoids the “expected-damage” trap of multiplying probabilities by an assumed damage curve.
• Ensemble (threshold 10 days): fraction of scenarios with 10 or fewer flood days.
Quinn et al. 2017.

## Slide 10
Objective 7 — NYC Storage Resilience (higher is better)
storage% = combined NYC storage ÷ 270,837 MG × 100%
f₇ = the 5th percentile of daily storage% (P₅)
• How low NYC storage routinely gets: the level that daily combined storage (Cannonsville + Pepacton + Neversink) stays above 95% of the time, as a percent of full capacity.
• A low percentile is a stable measure of “how depleted the system normally runs,” without the single-day minimum’s dependence on one drought event.
• Why the 5th percentile instead of the minimum: the minimum is dominated by a single event and is noisy; a low percentile is reproducible across scenarios.
• Ensemble (threshold 25%): fraction of scenarios whose 5th-percentile storage is at least 25%.
Quinn et al. 2017.