## Slide 1
Hazard-Space Scenario Selection for Robust Many-Objective Reservoir Policy Search in the Delaware River Basin
Summer 2026

## Slide 2: Content
Motivation & Literature Review
Proposal
  Hypothesis
  Research Questions
  Planned Contributions
Experimental Design
  Re-evaluation under climate change uncertainty
MOEA Problem Formulation
  Decision Variables
  Objectives
Supplemental
  Anvil scaling experiments
  Parametric sampling of uncertain monthly streamflow changes

## Slide 3
Motivation

## Slide 4: Motivation & Literature Review
Motivation:
0. Scenario design is a key part of robustness frameworks and influences results.

## Slide 5: Motivation & Literature Review
Figure from Jazmines dissertation
Motivation:
1. Large stochastic ensembles of streamflows are necessary for capturing the full range of hydrologic conditions resulting from natural variability.

## Slide 6: Motivation & Literature Review
Motivation:
Historical period
Historical period
Max drought magnitude
Kirsch-Nowak ensemble of increasing size

## Slide 7: Motivation & Literature Review
Motivation:
3. When using long stochastic sequences much of the simulation period may be low-stress and require simulation/compute time that is not contributing meaningfully to improving solutions.
Eg., in the current stochastic ensembles 84-93% of ensemble years are in Normal conditions.

## Slide 8: Motivation & Literature Review
Motivation:
4. There can be redundancy in streamflow scenarios resulting from sampling uncertain hydrologic drivers/forcings.
Hydro Uncertainty 1
Hydro Uncertainty 2
Hazard Measure 1
Hazard Measure 2

## Slide 9: Motivation & Literature Review
Motivation:
0. Scenario design is a key part of robustness frameworks and influences results.
1. Large stochastic ensembles of streamflows are necessary for capturing the full range of hydrologic conditions resulting from natural variability.
2. Large stochastic ensembles of streamflows are necessary for capturing the full range of hydrologic conditions resulting from natural variability.
3. When using long stochastic sequences much of the simulation period may be low-stress and require simulation/compute time that is not contributing meaningfully to improving solutions.
  Eg., in the current stochastic ensembles 84-93% of ensemble years are in Normal conditions.
4. There can be redundancy in streamflow scenarios resulting from sampling uncertain hydrologic drivers/forcings.
5. Rare, extreme drought hazard events drive the most consequential outcomes.

## Slide 10: Motivation & Literature Review
Motivation:
6. There is interest in finding efficient subsamples of the scenario space that produce more robust solutions.
Antecedent | Established | Limitations
Cohen et al. 2021 | training-scenario properties drive out-of-sample robustness | Requires problem-driven regret selection; a preliminary perfect-foresight MOEA run for each scenario
Zaniolo et al. 2023 | drought-type training ensembles change the policies found | Hazard metrics imposed a priori before generation; hazards aren’t emergent
Zatarain Salazar et al. 2017 | search-ensemble size vs fidelity vs cost tradeoffs | Scenario selection relies on 1-dimensional aggregate mean flow CDF sampling
Bonham et al. 2024 | space-filling subsampling + coverage metrics in water resources | Post-hoc robustness ranking, not the search ensemble

## Slide 11: Motivation & Literature Review
I. Trace-based
Historic series, single traces, design events
II. Distribution-driven
sample an assumed distribution
III. Bottom-up coverage
span a deeply uncertain parameter space
IV. Problem-driven
select by decision relevance
value
Uncertain param A
Uncertain param B
Density
Value
Time
Obj A
Obj B
Common scenario design approaches used in the water resources optimization literature.

## Slide 12: Proposal: Hypothesis
Idea:
Create a space-filling sample of the hazard space, evaluate candidate policies using this deeply uncertain hazard space.
Hazard Measure 1
Hazard Measure 2
Hazard Measure 1
Hazard Measure 2

## Slide 13: Proposal: Hypothesis
Idea:
Create a space-filling sample of the hazard space, evaluate candidate policies using this deeply uncertain hazard space.
Hazard Measure 1
Hazard Measure 2
Hazard Measure 1
Hazard Measure 2
Hazard Measure 1
Hazard Measure 2
Hazard Measure 1
Hazard Measure 2

## Slide 14: Proposal: Hypothesis
Antecedent | Established | Limitations
Cohen et al. 2021 | training-scenario properties drive out-of-sample robustness | Requires problem-driven regret selection; a preliminary perfect-foresight MOEA run for each scenario
Zaniolo et al. 2023 | drought-type training ensembles change the policies found | Hazard metrics imposed a priori before generation; hazards aren’t emergent
Zatarain Salazar et al. 2017 | search-ensemble size vs fidelity vs cost tradeoffs | Scenario selection relies on 1-dimensional aggregate mean flow CDF sampling
Bonham et al. 2024 | space-filling subsampling + coverage metrics in water resources | Post-hoc robustness ranking, not the search ensemble
No study builds the MOEA search ensemble by space-filling selection in a multi-dimensional hazard space and tests it on a held-out ensemble spanning deep climate uncertainty.
Comparison with relevant and recent publications:

## Slide 15: Proposal: Hypothesis
Input space generator & climate-forcing parameters θ
generate
Hazard space drought / low-flow / high-flow metrics per sequence
simulate
Outcome space objective values of a policy under a scenario
hazard metrics are measured on realized sequences, before any simulation (drought event metrics; flow indices)
so hazard-space ensemble design is a simulation-free, pre-optimization step, reusable across problem formulations
Not a good slide, not good narrative

## Slide 16
NYC Reservoir Operations
Problem Formulation: Decision Variables

## Slide 17: MOEA Problem Formulation: Decision Variables
Overview of the FFMP operational rules
Max NYC & NJ Diversion Limits
Minimum Flow Target at Montague
The Supreme Court established:
The Flexible Flow Management Program (FFMP, 2017) was established, via unanimous consent from the Decree parties, to provide flexibility to these requirements during periods of drought to alleviate water stress.
The FFMP recognizes the inherent tension between water diversions and downstream flow targets.
As drought stress increases:
NYC and NJ diversion allocations decrease, leading to municipal supply curtailment
Montague (and Trenton) streamflow targets decrease, leading to downstream environmental and supply risk.
The Court requires unanimous agreement from all DRBC Decree parties to modify these requirements.

## Slide 18: MOEA Problem Formulation: Decision Variables
Overview of the FFMP operational rules
Baseline Max NYC & NJ Diversion Limits
Baseline Minimum Flow Target at Montague
Minimum Daily Reservoir Releases (L3-L5)
NYC Reservoir Spill Mitigation Releases (L1)
Court Mandated (unchanged, fixed)
Montague & Trenton flow target reduction (L3-L5)
Allowable NYC & NJ diversion reduction (L3-L5)
NYC storage zones dictate operational rules
Storage Zone
Determines

## Slide 19: MOEA Problem Formulation: Decision Variables
NYC Reservoir Operational Decision Variables:
Storage Zone Boundary Vertical Shifts
Storage Zone Boundary Temporal Shift
Combined NYC Storage
Combined NYC Storage
One vertical shift per zone plateau
One temporal shift per zone
±30-days
±10%

## Slide 20: MOEA Problem Formulation: Decision Variables
NYC Reservoir Operational Decision Variables:
Storage Zone Boundary Vertical Shifts
Storage Zone Boundary Temporal Shift
NYC Diversion Reduction Factor
NJ Diversion Reduction Factor
Supreme Court Allocation
Supreme Court Allocation
±15% FFMP values
±15% FFMP values

## Slide 21: MOEA Problem Formulation: Decision Variables
NYC Reservoir Operational Decision Variables:
Storage Zone Boundary Vertical Shifts
Storage Zone Boundary Temporal Shift
NYC Diversion Reduction Factor
NJ Diversion Reduction Factor
Montague & Trenton Streamflow Target Reduction Factor

## Slide 22: MOEA Problem Formulation: Decision Variables
NYC Reservoir Operational Decision Variables:
Storage Zone Boundary Vertical Shifts
Storage Zone Boundary Temporal Shift
NYC Diversion Reduction Factor
NJ Diversion Reduction Factor
Montague & Trenton Streamflow Target Reduction Factor
Spill Mitigation Releases

## Slide 23: MOEA Problem Formulation: Decision Variables
NYC Reservoir Operational Decision Variables:
Storage Zone Boundary Vertical Shifts
Storage Zone Boundary Temporal Shift
NYC Diversion Reduction Factor
NJ Diversion Reduction Factor
Montague & Trenton Streamflow Target Reduction Factor
Spill Mitigation Releases
Minimum Daily Release Scaling Factor

## Slide 24: MOEA Problem Formulation: Decision Variables
Decision variable group (n) | Plain-language description | Bounds
NYC drought delivery factors (3) | Fraction of NYC's diversion allowed in each of the three drought stages | FFMP value ± 0.15, clipped at 1.0
NJ drought delivery factors (2) | Fraction of NJ's diversion allowed in the two deepest drought stages | FFMP value ± 0.15, clipped at 1.0
Storage-zone void shifts (6) | Raise/lower the fall–winter low plateau of each storage-zone boundary curve | ±0.10 of capacity (upper zone: +0.025)
Storage-zone refill shifts (3) | Raise/lower the spring refill target of the drought-zone curves only | ±0.10 of capacity
Storage-zone temporal shifts (6) | Slide each zone-boundary curve earlier/later in the year | ±30 days
Flood-release scales (6) | Scale each reservoir's flood-zone spill-mitigation release schedule | 0.5 – 1.2/1.35/1.55 (upper zone); 0.5 – 2.0 (lower zone)
Seasonal minimum-release scales (4) | Scale conservation-zone daily release profiles by FFMP season | 0.8 – 2.6
Flow-target factor scales (6) | Scale Montague/Trenton drought-stage flow-target reductions | 0.65 – 1.15
Table 1. FFMP Decision Variables (36 total)

## Slide 25: MOEA Problem Formulation: Decision Variables
Overview of the FFMP operational rules
Storage zones
Minimum daily release requirements
NYC & NJ allocation reductions
Montague & Trenton flow target reductions
Daily releases while in flood zone

## Slide 26: MOEA Problem Formulation: Decision Variables
Example visualizing a custom set of decision variables and the resulting policy rules.
Dashed lines = Default FFMP
Solid lines = Custom operating rules

## Slide 27
NYC Reservoir Operations
Problem Formulation: Objective Functions

## Slide 28: MOEA Problem Formulation: Objective Definitions
NYC objective definition notes:
Focused on re-optimizing the flexible flow management program (i.e., changes to operations in drought zones) and not the Court mandated NYC & Montague diversions
    As a result, objectives are defined relative to the 1954 Supreme Court mandated requirements
Currently not planning on using salt-front objectives since the SalinityLSTM does not extrapolate well above river mile ~95.

## Slide 29: MOEA Problem Formulation: Objective Definitions
Current objective definition set
Realization 1
Realization 2
Realization N
…
Year 1
Year 2
Year N
…

## Slide 30: MOEA Problem Formulation: Objective Definitions
Current objective definition set
Realization 1
Realization 2
Realization N
…
Year 1
Year 2
Year N
…
Each objective is calculated using:
Step 1: Annual metric
Step 2: Aggregation metric across all ensemble years

## Slide 31: MOEA Problem Formulation: Objective Definitions
Objective (direction) | Mathematical description | Description | Units | ε
NYC delivery reliability (max) | Frequency of years with < 3 failure weeks (delivery ≥ 99% of entitlement) | How often NYC's water supply is satisfied | fraction of years | 0.02
NYC delivery deficit (min) | Worst 1st-percentile year of within-year CVaR₉₀ weekly deficit | Depth of NYC's worst supply shortfalls | % of 800 MGD | 2.0
Montague flow reliability (max) | Frequency of years with < 3 failure weeks (flow ≥ 1,131 MGD) | How often the Decree flow target is met | fraction of years | 0.02
Montague flow deficit (min) | Worst 1st-percentile year of within-year CVaR₉₀ weekly deficit | Depth of the worst Montague flow shortfalls | % of target | 1.5
Trenton flow reliability (max) | Frequency of years with < 1 failure week (flow ≥ 1,939 MGD) | How often the salt-front–repelling flow objective is met | fraction of years | 0.015
Downstream flood exceedance (min) | Mean annual Σ over days of max-across-gauges (stage − NWS minor flood stage)⁺ | Magnitude of downstream flooding above minor flood stage | ft·days/yr | 0.01*
NYC minimum storage (max) | Worst 1st-percentile year of annual minimum daily aggregate storage | How low the reservoirs are drawn down | % of capacity | 5.0
NJ delivery reliability (max) | Frequency of years with < 1 failure week (delivery ≥ 99% of entitlement) | How often NJ's water supply is satisfied | fraction of years | 0.025
Table 2. The Eight Optimization Objectives

## Slide 32: MOEA Problem Formulation: Objective Definitions
There is minimal, and frequently negative, spearman correlation between objectives.

## Slide 33
NYC Reservoir Re-Operation
Preliminary Results

## Slide 34: MOEA Problem Formulation: Objective Definitions
Preliminary results are based on:
50k NFE (~2hr runtime)
2x MMBorg seeds
Optimized under historic streamflow scenario (1945-2023)
WARNING: Preliminary results do not converge.

## Slide 35: MOEA Problem Formulation: Objective Definitions
1761 pareto-approximate solutions merged across seeds

## Slide 36: MOEA Problem Formulation: Objective Definitions
75/1761 (4.3%) of pareto-approximate solutions fully dominate the baseline FFMP performance

## Slide 37: MOEA Problem Formulation: Objective Definitions

## Slide 38
Experimental Design

## Slide 39: Experimental Design

## Slide 40
Experimental Design:
Alternative Scenario Designs

## Slide 41: Experimental Design: Optimization Evaluation Scenarios
Design | Generation Method | Ensemble size (per optimization evaluation)
Historical (HIST) | Observed record simulated as one continuous realization; reference for prevailing practice | 1 realization × 77 yr (77 scenario-years)
Probabilistic Sample (PS) | i.i.d. samples from the stationary Kirsch–Nowak stochastic generator | 100 realizations × 10 yr (1,000 scenario-years)
Hazard Filling (HF) | Proposed design: space-filling selection from a 10⁶-member candidate ensemble for coverage of the hydrologic hazard space | 100 realizations × 10 yr, selected from 10⁶ candidates
Re-evaluation ensemble | Latin hypercube sample of deeply uncertain climate forcings (CMIP6-informed) crossed with stochastic realizations | 1,000 SOWs × 25 realizations × 50 yr (25,000 realizations)
Table 3. Scenario Designs and Ensemble Sizes
PS and HF share the generator, ensemble size, record length, and 500,000-NFE search budget; K = 3 construction replicates × 2 seeds per design.

## Slide 42: Experimental Design: Optimization Evaluation Scenarios
Hazard metric | Mathematical Definition | Description
Drought deficit volume |  | Cumulative SSI-6 deficit of the controlling drought event (SSI-months)
Drought peak depth |  | Most negative SSI-6 value reached (std. deviations)
Drought onset rate |  | Peak depth per month of drought intensification
Drought recovery rate |  | Peak depth per month of drought recovery
Flood peak magnitude |  | Maximum daily flow, normalized by the historical mean flow
Flood pulse duration |  | Consecutive days above the historical 95th-percentile flow around the peak
Hazard metric | Mathematical Definition | Description
Drought deficit volume |  | Cumulative SSI-6 deficit of the controlling drought event (SSI-months)
Drought peak depth |  | Most negative SSI-6 value reached (std. deviations)
Drought onset rate |  | Peak depth per month of drought intensification
Drought recovery rate |  | Peak depth per month of drought recovery
Flood peak magnitude |  | Maximum daily flow, normalized by the historical mean flow
Flood pulse duration |  | Consecutive days above the historical 95th-percentile flow around the peak
Table 4. Hydrologic Hazard Metrics for the Hazard-Filling Design
Computed on aggregate NYC reservoir inflow before any simulation; drought events identified by SSI-6 (controlling event = largest deficit volume).

## Slide 43
Experimental Design:
Re-evaluation under future hydrologic uncertainty

## Slide 44: Planned Methods

## Slide 45: Experimental Design: Re-evaluation under climate change uncertainty
Inspired by parametric harmonic formulation from Quinn et al. (2018).
Instead of parameterizing the log-space streamflow, parameterize the relative change in streamflow

## Slide 46: Experimental Design: Re-evaluation under climate change uncertainty
Can a 3 parameter harmonic capture CMIP6 informed monthly flow changes?

## Slide 47: Experimental Design: Re-evaluation under climate change uncertainty
Range & spread of harmonic parameters for all of the CMIP6 streamflow traces (same data as paper 2)
Fit the 3-parameter harmonic to each trace using OLS.

## Slide 48: Experimental Design: Re-evaluation under climate change uncertainty

## Slide 49: Experimental Design: Re-evaluation under climate change uncertainty

## Slide 50: Experimental Design: Re-evaluation under climate change uncertainty
Grey = LHS samples inside the hypercube containing 90% of CMIP6 scenarios
Color markers = fitted parameters from LHS ensemble

## Slide 51: Experimental Design: Re-evaluation under climate change uncertainty

## Slide 52: Experimental Design: Re-evaluation under climate change uncertainty

## Slide 53: Experimental Design: Re-evaluation under climate change uncertainty

## Slide 54
Supplemental

## Slide 55
Supplemental:
Parametric Sampling of Uncertain
Monthly Streamflow Change Factors

## Slide 56
Supplemental:
Anvil Scaling Experiments

## Slide 57: Anvil Scaling Experiment
Parallelism & Efficiency Levers:
Number of nodes
Number of core per node
Number of MM-Borg islands & workers
Number of realizations per Pywr-DRB simulation (pywr internal parallel)

## Slide 58: Anvil Scaling Experiment
Goal: Before committing to large scale MM-Borg optimization, measure (a) how densely we can pack model evaluations on a node and (b) how well MM-Borg's parallelism scales.
Anvil node: 128 cores, 256 GB
Test 1: Efficiency of running K workers on a single node with.
On one node, run K independent copies of the MM-Borg worker evaluation (a 20-realization, 20-year synthetic streamflow ensemble through Pywr-DRB). Each rank times one ‘cold’ + several warm evaluations and records peak memory. Sweeping K reveals when contention or memory becomes the limit.
Test 2: MM-Borg strong scaling.
MM-Borg runs at a fixed budget of 1,280 evaluations, using a short simulation window (~6 s/eval) so runs are cheap. Geometries: 8, 16, 32, 64 workers on one island, plus 2×32 and 4×16 island splits at 64 slots. Two random seeds each. Wall time to finish the fixed budget gives speedup and parallel efficiency.

## Slide 59: Anvil Scaling Experiments
Run K copies of the evaluation at the same time, K = 1, 8, 16, 32, 48, 64, 96, 128 core.
Every rank times one "cold" evaluation (first one, caches empty) then several "warm" ones, using the exact code path a Borg worker uses.
Question: does crowding more evaluations onto one node make each one slower?
Run = 20 realizations x 20 years

## Slide 60: Anvil Scaling Experiments
Packing is nearly free up to K=32 (only 1% slower than running alone), then costs 17% at full density K=128 (64.0 s -> 74.7 s).
However, a 17% per-evaluation penalty is worth it for 128× the parallelism.
Run = 20 realizations x 20 years

## Slide 61: Anvil Scaling Experiments
Top panel: Evaluations completed per node-hour, rising almost linearly with K to a maximum at K=128.
Bottom panel: SUs burned per 1,000 evaluations, decreasing as K rises and flattening out well before K=128 (open squares show the unbatched B=1 case for contrast).
Run = 20 realizations x 20 years

## Slide 62: Anvil Scaling Experiments
Take-aways
Top: Throughput scales nearly linearly (56 evals/node-hr at K=1 to 6,166 at K=128), about 110x.
The 17% per-evaluation slowdown never overtakes the parallelism benefit.
Bottom: Cost per 1,000 evaluations drops from 2,275 SU to 21 SU.
Most of the savings arrive by K~=40; beyond that the curve is flat, so K=128 is good but also okay if we need to use less (due to memory)
Run = 20 realizations x 20 years

## Slide 63: Anvil Scaling Experiments
Left panel: Peak memory used by a single rank across packing densities, for the typical (median) and worst (max) rank memory usage.
Right panel: Total node memory implied by K ranks at the worst-case per-rank footprint, against the 256 GB node limit (red dashed line).
Run = 20 realizations x 20 years

## Slide 64: Anvil Scaling Experiments
Short 4 year simulation, 1,280 NFE, 2 random seeds
Left panel: Wall time to finish the fixed evaluation budget as evaluation slots increase from 8 to 64 (log-log).
Middle panel: Speedup relative to the smallest 8-slot run, against the ideal linear line, with the two multi-island geometries overlaid.
Right panel: Parallel efficiency (fraction of ideal speedup retained) as slots increase.

## Slide 65: Anvil Scaling Experiments
Projected runtime combines the two measured pieces:
Evalutation runtime pack at K*=128 ranks/node
Borg scaling efficiency (assume 73% parallel efficiency)
For 750k NFE, 16 nodes and 4 islands:
= ~23k SU
= 10.5 hr

## Slide 66: Anvil Scaling Experiment
Setup Anvil allocation calculator (based on Lillian’s advice)
Based on results of runtime & scaling experiments and experimental settings, estimate the total SUs needed for optimizations.
Current scale assumptions:
Optimization
500k NFE
1,000 years per evaluation
3x formulation designs
5x seeds per design
Re-evaluation
1,500 solutions re-evaluated
10,000 realizations x 100 years (1M years) per solution

## Slide 67: Anvil Scaling Experiment
Setup Anvil allocation calculator (based on Lillian’s advice)
Chart: Service Unit Split
| search_su | reeval_su | UNUSED ALLOCATION
 | 497266.5104 | 85205.3157 | 167528.1738
15 optimizations total:
3 formulations x 5 seeds
Uses ~500 SU of allocation
Saving some budget for re-runs if needed

## Slide 68: Anvil Scaling Experiment
Setup Anvil allocation calculator (based on Lillian’s advice)
Chart: Estimated Wallclock Runtime
| search_walltime_parallel_hr | reeval_walltime_hr
 | 8.0935 | 20.8021
Wallclock time assuming use of 32 full nodes for each run.
8hr per optimization run/seed
Total = (8x15hr) if all of them are run in serial.

## Slide 69: Anvil Scaling Experiments
Left panel: Wall time per evaluation as B increases, for an isolated rank and a fully-packed node.
Middle panel: Peak per-rank memory as B increases.
Right panel: SU cost per 1,000 evaluations as B increases.
Run = 20 realizations x 20 years

## Slide 70: Anvil Scaling Experiments

## Slide 71: Anvil Scaling Experiments

## Slide 72
Archive (possibly delete)

## Slide 73: Experimental Design
Scenario Design
Optimization
Historical trace (baseline)
Well characterized (probabilistic) ensemble generated from Kirsch-Nowak
MM-BorgMOEA
Approximate Pareto Front
Fixed (N-year, NFE) per optimization
5 seeds per run
Re-evaluation & Robustness
Re-evaluation of pareto-approximate solutions across large ensemble of climate change uncertainties
Multi-metric hazard space filling ensemble, sampled from very large stochastic ensemble
Multi-criteria satisficing robustness
Regret relative to default FFMP
Deeply uncertain hydrologic future ensemble
Approximate Pareto Front
Approximate Pareto Front

## Slide 74: Proposal: Hypothesis
Idea:
Create a space-filling sample of the hazard space, evaluate candidate policies using this deeply uncertain hazard space.
We can then combine this with factorial samples of other deeply uncertain factors.
Hazard Measure 1
Hazard Measure 2
X
X
X
Deeply uncertain with socioeconomic factors