## Slide 1
Proposal:
“NEW TITLE”
Summer 2026

## Slide 2: Content
Motivation & Literature Review
Proposal
  Hypothesis
  Research Questions
  Planned Contributions
Experimental Design
  Re-evaluation under climate change uncertainty
MOEA Problem Formulation
  Decision Variables
  Objectives
Supplemental
  Anvil scaling experiments
  Parametric sampling of uncertain monthly streamflow changes

## Slide 3: Motivation & Literature Review
Motivation:
0. Scenario design is a key part of robustness frameworks and influences results.

## Slide 4: Motivation & Literature Review
Figure from Jazmines dissertation
Motivation:
1. Large stochastic ensembles of streamflows are necessary for capturing the full range of hydrologic conditions resulting from natural variability.

## Slide 5: Motivation & Literature Review
Motivation:
2. Large stochastic ensembles of streamflows are necessary for capturing the full range of hydrologic conditions resulting from natural variability.
Historical period
Historical period
Max drought magnitude
Kirsch-Nowak ensemble of increasing size

## Slide 6: Motivation & Literature Review
Motivation:
3. When using long stochastic sequences much of the simulation period may be low-stress and require simulation/compute time that is not contributing meaningfully to improving solutions.
Eg., in the current stochastic ensembles 84-93% of ensemble years are in Normal conditions.

## Slide 7: Motivation & Literature Review
Motivation:
4. There can be redundancy in streamflow scenarios resulting from sampling uncertain hydrologic drivers/forcings.
Hydro Uncertainty 1
Hydro Uncertainty 2
Hazard Measure 1
Hazard Measure 2

## Slide 8: Motivation & Literature Review
Motivation:
5. Rare, extreme drought hazard events drive the most consequential outcomes.

## Slide 9: Motivation & Literature Review
Motivation:
6. There is interest in finding efficient subsamples of the scenario space that produce more robust solutions.
Antecedent | Established | Limitations
Cohen et al. 2021 | training-scenario properties drive out-of-sample robustness | Requires problem-driven regret selection; a preliminary perfect-foresight MOEA run for each scenario
Zaniolo et al. 2023 | drought-type training ensembles change the policies found | Hazard metrics imposed a priori before generation; hazards aren’t emergent
Zatarain Salazar et al. 2017 | search-ensemble size vs fidelity vs cost tradeoffs | Scenario selection relies on 1-dimensional aggregate mean flow CDF sampling
Bonham et al. 2024 | space-filling subsampling + coverage metrics in water resources | Post-hoc robustness ranking, not the search ensemble

## Slide 10: Motivation & Literature Review
I. Trace-based
Historic series, single traces, design events
II. Distribution-driven
sample an assumed distribution
III. Bottom-up coverage
span a deeply uncertain parameter space
IV. Problem-driven
select by decision relevance
value
Uncertain param A
Uncertain param B
Density
Value
Time
Obj A
Obj B
Common scenario design approaches used in the water resources optimization literature.

## Slide 11: Proposal: Hypothesis
Idea:
Create a space-filling sample of the hazard space, evaluate candidate policies using this deeply uncertain hazard space.
Hydro Uncertainty 1
Hydro Uncertainty 2
Hazard Measure 1
Hazard Measure 2
Hazard Measure 1
Hazard Measure 2

## Slide 12: Proposal: Hypothesis
Idea:
Create a space-filling sample of the hazard space, evaluate candidate policies using this deeply uncertain hazard space.
We can then combine this with factorial samples of other deeply uncertain factors.
Hazard Measure 1
Hazard Measure 2
X
X
X
Deeply uncertain with socioeconomic factors

## Slide 13: Proposal: Hypothesis
Antecedent | Established | Limitations
Cohen et al. 2021 | training-scenario properties drive out-of-sample robustness | Requires problem-driven regret selection; a preliminary perfect-foresight MOEA run for each scenario
Zaniolo et al. 2023 | drought-type training ensembles change the policies found | Hazard metrics imposed a priori before generation; hazards aren’t emergent
Zatarain Salazar et al. 2017 | search-ensemble size vs fidelity vs cost tradeoffs | Scenario selection relies on 1-dimensional aggregate mean flow CDF sampling
Bonham et al. 2024 | space-filling subsampling + coverage metrics in water resources | Post-hoc robustness ranking, not the search ensemble
Gap. No study builds the MOEA search ensemble by space-filling selection in a multi-dimensional hazard space and tests it on a held-out ensemble spanning deep climate uncertainty.
Comparison with relevant and recent publications:

## Slide 14: Proposal: Hypothesis
Input space generator & climate-forcing parameters θ
generate
Hazard space drought / low-flow / high-flow metrics per sequence
simulate
Outcome space objective values of a policy under a scenario
hazard metrics are measured on realized sequences, before any simulation (drought event metrics; flow indices)
so hazard-space ensemble design is a simulation-free, pre-optimization step, reusable across problem formulations

## Slide 15
Experimental Design

## Slide 16: Planned Methods
Scenario Design
MOEA Optimization
Historical trace (baseline)
Well characterized (probabilistic) ensemble generated from Kirsch Nowak
Ensemble generated by sampling deeply uncertain stream change parameters
Deep uncertainty hazard space-filling subsample ensemble
MM-BorgMOEA
Approximate Pareto Front
Fixed (N-year, NFE) per optimization
10 seeds per run
Robustness Comparison
Re-evaluation of pareto-approximate solutions across large ensemble of climate change uncertainties
Multi-metric hazard space filling ensemble, sampled from very large stochastic ensemble
Multi-criteria satisficing robustness
Regret metric (TBD)

## Slide 17: Experimental Design: Re-evaluation under climate change uncertainty
Inspired by parametric harmonic formulation from Quinn et al. (2018).
Instead of parameterizing the log-space streamflow, parameterize the relative change in streamflow

## Slide 18: Experimental Design: Re-evaluation under climate change uncertainty
Can a 3 parameter harmonic capture CMIP6 informed monthly flow changes?

## Slide 19: Experimental Design: Re-evaluation under climate change uncertainty
Range & spread of harmonic parameters for all of the CMIP6 streamflow traces (same data as paper 2)
Fit the 3-parameter harmonic to each trace using OLS.

## Slide 20: Experimental Design: Re-evaluation under climate change uncertainty

## Slide 21: Experimental Design: Re-evaluation under climate change uncertainty

## Slide 22: Experimental Design: Re-evaluation under climate change uncertainty
Grey = LHS samples inside the hypercube containing 90% of CMIP6 scenarios
Color markers = fitted parameters from LHS ensemble

## Slide 23: Experimental Design: Re-evaluation under climate change uncertainty

## Slide 24: Experimental Design: Re-evaluation under climate change uncertainty

## Slide 25: Experimental Design: Re-evaluation under climate change uncertainty

## Slide 26
NYC Reservoir Operations
Problem Formulation

## Slide 27: MOEA Problem Formulation: Decision Variables
Overview of the FFMP operational rules
Max NYC & NJ Diversion Limits
Minimum Flow Target at Montague
The Supreme Court established:
The Flexible Flow Management Program (FFMP, 2017) was established, via unanimous consent from the Decree parties, to provide flexibility to these requirements during periods of drought to alleviate water stress.
The FFMP recognizes the inherent tension between water diversions and downstream flow targets.
As drought stress increases:
NYC and NJ diversion allocations decrease, leading to municipal supply curtailment
Montague (and Trenton) streamflow targets decrease, leading to downstream environmental and supply risk.
The Court requires unanimous agreement from all DRBC Decree parties to modify these requirements.

## Slide 28: MOEA Problem Formulation: Decision Variables
Overview of the FFMP operational rules
Baseline Max NYC & NJ Diversion Limits
Baseline Minimum Flow Target at Montague
Minimum Daily Reservoir Releases (L3-L5)
NYC Reservoir Flood Prevention Operations (L1)
Court Mandated (unchanged, fixed)
Montague flow target reduction (L3-L5)
Allowable NYC & NJ diversion reduction (L3-L5)
NYC storage zones dictate operational rules
Storage Zone
Determines

## Slide 29: MOEA Problem Formulation: Decision Variables
Overview of the FFMP operational rules
Storage zones
Minimum daily release requirements
NYC & NJ allocation reductions
Montague & Trenton flow target reductions
Daily releases while in flood zone

## Slide 30: MOEA Problem Formulation: Decision Variables
Type | No. of Variables | Description
Storage Zone Boundary Vertical Shifts | x 6 zones x 4 points = 24 | Mean + cosine + sine components (3 each) of a single annual harmonic for each of the 6 storage-zone threshold curves L1b–L5. Raise/lower the rule curves as a fraction of capacity, evaluated at each curve's own corner date
Storage Zone Boundary Temporal Shift | x 6 zones x 4 points = 24 | Day-of-year phase shift (±30 days) for each of the 6 zone-boundary curves
Montague & Trenton Streamflow Target Reduction Factor | (2 zones + 1 zone x 4 seasons) x 2 flow targets = 8 | Multipliers on the Montague/Trenton monthly flow-target factor tables
NYC Diversion Reduction Factor | x 3 zones | Fractional multipliers on the NYC diversion entitlement for the three drought stages
NJ Diversion Reduction Factor | x 2 zones | Fractional multipliers on the NJ diversion entitlement for L4-L5 drought stages
Flood Mitigation Releases | x 3 reservoirs x 2 zones = 6 | Multipliers on the default L1a/L1b flood-release schedule
Minimum Daily Release Scaling Factor | x 4 seasons | One multiplier per FFMP on the conservation-zone (L1c-and-below) minimum-release baseline schedules across all three reservoirs
 | = 63 decision variables | 

## Slide 31: MOEA Problem Formulation: Decision Variables

## Slide 32: MOEA Problem Formulation: Decision Variables
Visualizing random decision variables and the resulting policy rules

## Slide 33: MOEA Problem Formulation: Decision Variables
Visualizing random decision variables and the resulting policy rules

## Slide 34: MOEA Problem Formulation: Decision Variables
Type
Storage Zone Boundaries
Streamflow Target at Montague
Allowable NYC Diversion
Flood Mitigation Releases
Minimum Daily Releases

## Slide 35: MOEA Problem Formulation: Decision Variables
Operational parameters: NYC storage zones
  Vertical Shift (+/- 10%)
  Temporal Shift (+/- 30 days)

## Slide 36: MOEA Problem Formulation: Decision Variables
Operational parameters: Minimum daily release

## Slide 37: MOEA Problem Formulation: Decision Variables
Operational parameters:
NYC Storage Zones (L1a-L5)
Minimum daily release
  For each season:
    Scale magnitude (+/- 10%)
    Temporal shift (+/- 30 days)

## Slide 38: MOEA Problem Formulation: Objective Definitions
NYC objective definition notes:
Focused on re-optimizing the flexible flow management program (i.e., changes to operations in drought zones) and not the Court mandated NYC & Montague diversions
    As a result, objectives are defined relative to the 1954 Supreme Court mandated requirements
Currently not planning on using salt-front objectives since the SalinityLSTM does not extrapolate well above river mile ~95.

## Slide 39: MOEA Problem Formulation: Objective Definitions
Description | Definition for Single-Trace Evaluation
O1: NYC Delivery Reliability | Percentage of simulated weeks when NYC diversion >= 99% of demand (capped at 800MGD; Decree)
O2: NYC Delivery Shortage Vulnerability | Average shortage for the worst 10% of shortage weeks
O3: Montague Flow Reliability | Percentage of simulated weeks with Montague flow above 1131MGD (Decree)
O4: Montague Flow Shortage Vulnerability | Average shortage for the worst 10% of shortage weeks
O5: Trenton Flow Reliability | Percentage of simulated weeks with Trenton flow above 1938MGD
O6: Flood Days Below NYC Reservoirs | Number of days that any of the 3 NYC flood gauges > “major flood” stage
O7: Minimum NYC Storage Outcomes | Lowest 5% storage

## Slide 40: MOEA Problem Formulation: Objective Definitions
There is minimal, and frequently negative, spearman correlation between objectives.

## Slide 41: MOEA Problem Formulation: Objective Definitions
A small random sample (24) of decision variables reveals improvements in performance are possible (with tradeoffs potentially necessary).
Current FFMP rules prioritize NYC diversion reliability

## Slide 42
Supplemental

## Slide 43
Supplemental:
Anvil Scaling Experiments

## Slide 44: Anvil Scaling Experiment
Parallelism & Efficiency Levers:
Number of nodes
Number of core per node
Number of MM-Borg islands & workers
Number of realizations per Pywr-DRB simulation (pywr internal parallel)

## Slide 45: Anvil Scaling Experiment
Goal: Before committing to large scale MM-Borg optimization, measure (a) how densely we can pack model evaluations on a node and (b) how well MM-Borg's parallelism scales.
Anvil node: 128 cores, 256 GB
Test 1: Efficiency of running K workers on a single node with.
On one node, run K independent copies of the MM-Borg worker evaluation (a 20-realization, 20-year synthetic streamflow ensemble through Pywr-DRB). Each rank times one ‘cold’ + several warm evaluations and records peak memory. Sweeping K reveals when contention or memory becomes the limit.
Test 2: MM-Borg strong scaling.
MM-Borg runs at a fixed budget of 1,280 evaluations, using a short simulation window (~6 s/eval) so runs are cheap. Geometries: 8, 16, 32, 64 workers on one island, plus 2×32 and 4×16 island splits at 64 slots. Two random seeds each. Wall time to finish the fixed budget gives speedup and parallel efficiency.

## Slide 46: Anvil Scaling Experiments
Run K copies of the evaluation at the same time, K = 1, 8, 16, 32, 48, 64, 96, 128 core.
Every rank times one "cold" evaluation (first one, caches empty) then several "warm" ones, using the exact code path a Borg worker uses.
Question: does crowding more evaluations onto one node make each one slower?
Run = 20 realizations x 20 years

## Slide 47: Anvil Scaling Experiments
Packing is nearly free up to K=32 (only 1% slower than running alone), then costs 17% at full density K=128 (64.0 s -> 74.7 s).
However, a 17% per-evaluation penalty is worth it for 128× the parallelism.
Run = 20 realizations x 20 years

## Slide 48: Anvil Scaling Experiments
Top panel: Evaluations completed per node-hour, rising almost linearly with K to a maximum at K=128.
Bottom panel: SUs burned per 1,000 evaluations, decreasing as K rises and flattening out well before K=128 (open squares show the unbatched B=1 case for contrast).
Run = 20 realizations x 20 years

## Slide 49: Anvil Scaling Experiments
Take-aways
Top: Throughput scales nearly linearly (56 evals/node-hr at K=1 to 6,166 at K=128), about 110x.
The 17% per-evaluation slowdown never overtakes the parallelism benefit.
Bottom: Cost per 1,000 evaluations drops from 2,275 SU to 21 SU.
Most of the savings arrive by K~=40; beyond that the curve is flat, so K=128 is good but also okay if we need to use less (due to memory)
Run = 20 realizations x 20 years

## Slide 50: Anvil Scaling Experiments
Left panel: Peak memory used by a single rank across packing densities, for the typical (median) and worst (max) rank memory usage.
Right panel: Total node memory implied by K ranks at the worst-case per-rank footprint, against the 256 GB node limit (red dashed line).
Run = 20 realizations x 20 years

## Slide 51: Anvil Scaling Experiments
Short 4 year simulation, 1,280 NFE, 2 random seeds
Left panel: Wall time to finish the fixed evaluation budget as evaluation slots increase from 8 to 64 (log-log).
Middle panel: Speedup relative to the smallest 8-slot run, against the ideal linear line, with the two multi-island geometries overlaid.
Right panel: Parallel efficiency (fraction of ideal speedup retained) as slots increase.

## Slide 52: Anvil Scaling Experiments
Projected runtime combines the two measured pieces:
Evalutation runtime pack at K*=128 ranks/node
Borg scaling efficiency (assume 73% parallel efficiency)
For 750k NFE, 16 nodes and 4 islands:
= ~23k SU
= 10.5 hr

## Slide 53: Anvil Scaling Experiment
Setup Anvil allocation calculator (based on Lillian’s advice)
Based on results of runtime & scaling experiments and experimental settings, estimate the total SUs needed for optimizations.
Current scale assumptions:
Optimization
500k NFE
1,000 years per evaluation
3x formulation designs
5x seeds per design
Re-evaluation
1,500 solutions re-evaluated
10,000 realizations x 100 years (1M years) per solution

## Slide 54: Anvil Scaling Experiment
Setup Anvil allocation calculator (based on Lillian’s advice)
Chart: Service Unit Split
| search_su | reeval_su | UNUSED ALLOCATION
 | 497266.5104 | 85205.3157 | 167528.1738
15 optimizations total:
3 formulations x 5 seeds
Uses ~500 SU of allocation
Saving some budget for re-runs if needed

## Slide 55: Anvil Scaling Experiment
Setup Anvil allocation calculator (based on Lillian’s advice)
Chart: Estimated Wallclock Runtime
| search_walltime_parallel_hr | reeval_walltime_hr
 | 8.0935 | 20.8021
Wallclock time assuming use of 32 full nodes for each run.
8hr per optimization run/seed
Total = (8x15hr) if all of them are run in serial.

## Slide 56: Anvil Scaling Experiments
Left panel: Wall time per evaluation as B increases, for an isolated rank and a fully-packed node.
Middle panel: Peak per-rank memory as B increases.
Right panel: SU cost per 1,000 evaluations as B increases.
Run = 20 realizations x 20 years

## Slide 57: Anvil Scaling Experiments

## Slide 58: Anvil Scaling Experiments

## Slide 59
Supplemental:
Parametric Sampling of Uncertain
Monthly Streamflow Change Factors